Item of quotation: 10

Specification of: RLM E3-3540-23-19-C

Direct driven high-performance centrifugal fan RLM Evo with PREMIUM EFFICIENCY motor in efficiency class IE 3 (IEC 60034-30)

Complete assembly module with highest system efficiency, specifically developed and optimized for use without a spiral casing. Newly developed high performance impeller with optimized shape and highest efficiency, comprising six backward curved hollow section true aerofoil blades with real turbulence profile and rounded, inclined blade leading edges from impeller shroud to back plate, for optimal impact over the entire width of the blade. Co-rotating radial diffuser with optimized exit curving on the cover disc to enhance efficiency. Impeller made of high tensile sheet steel in an automated manufacturing process, robotic welding, degreased, iron phosphated and coated with a high quality epoxy-polyester mixed powder, fastened with a clamping bush to the shaft of the foot motor, balanced statically and dynamically according to DIN ISO 21940-11. System inlet cone made of galvanized sheet steel for optimal inflow to the impeller, equipped with flow measuring device IMV as a standard feature. Attached internal rotor motor, IM B5 mounting arrrangement, with efficient asynchronous technology with 3 PTCs suitable for operation on the drive (VFD), optimally coordinated with the high performance impeller. Complete module optimally adjusted, built to a supporting structure, prepared for vibration decoupling. Fan for vertical installation and airflow in upward direction. Performance data (w/o drive) according to tolerance class 1 to DIN 24 166.

Technical data of the fan: RLM E3-3540-23-19-C	fulfills the ErP requirements 2015

| Description | Value Dimension |
| --- | --- |
| Specified duty point |  |
| Design duty point |  |
| Installation acc. DIN 24163 Part 1 | A |
| Reference density (Rho1) | 1.20 kg/m³ |
| Medium temperature (t) | 20 C |
| Fan weight | 53 kg |
| Feed data |  |
| Main's frequency (fN) | 50 Hz |
| Voltage (UN) | 400 V |
| Rated motor data |  |
| Phases-Voltage-Frequency | 3~400 D-50 V-Hz |
| Frame size-No of poles: | 112M / IE3-2 |
| Power (PN) | 4 kW |
| Speed (nN | 2905 min-1 |
| Current (IN) | 7,45 A |
| operational limits |  |
| Max. fan speed (nvmax) | 3150 min-1 |
| Max. operating frequency (fmax) | 54 Hz |
| Temperature range for conveying medium (tmin ...tmax) | -20...40 C |
| ErP-Data at best efficiency and density - kg/m^3 |  |
| measurement- / efficiency category | A / static |
| design status of VSD | has to be installed |
| overall efficiency (ETAopt) | 67.4 % |
| achieved efficiency grade (Nist) | 71.2 |
| required efficiency grade in 2013 / 2015 (N) | 58 / 62 |
| Air flow rate (Vopt) | 6679 m³/h |
| pressure rise (dpopt) | 1580 Pa |
| Fan speed (nvopt) | 3150 min-1 |
| motor power input (P1opt) | 4.35 kW |
| specific ratio (ddpopt) | 1.016 |

Fan curve to RLM E3-3540-23-19-C

Dimensions to RLM E3-3540-23-19-C

Rotation:	RD

Handing:	90